LA VERSION FRANCAISE SUIVRA PROCHAINEMENT

DGRB/DGSE

Technical Information Service
Catalog Item 20
Broadcast Data Extract (AM-FM-TV)

USER MANUAL
Version 3.0

Revised September 1994

Original by:	Jean-Marc Paquet
Revisions by: J.-M. Paquet/D.Bergeron/G.Wood
Filename:	M:\OPER\MANUALS\BDBS_EXT.WP

BROADCAST DATA EXTRACT (AM-FM-TV)

USER MANUAL

TABLE OF CONTENTS

PAGE

1.0 INTRODUCTION 1
1.1 Changes 1

2.0 DISTRIBUTION AND MEDIA 1

3.0 DATA AND FILE ORGANIZATION 1
3.1 Data Restrictions 1
3.2 File Organization 2

4.0 ANTENNA PATTERNS 3
4.1 Omnidirectional Patterns 8
4.2 Vertical Patterns 8
4.3 "THEORETICAL " Patterns 9
4.4 "BRIEF"/"PRECISE" Patterns 9

5.0 FUTURE PLANS 9

6.0 ALS DATA EXTRACT 9

7.0 SUPPORT UTILITIES 9

8.0 CONTOURS ACCURACY 10

APPENDIX 1 11

A.0 CONDUMP PROGRAM 11
A.1 dBASE-to-ASCII Batch File 11
A.2 Program Inputs 11
A.3 Program Outputs 12
A.4 Technical Requirements 13
A.5 CONFIG.SYS 13

B.0 INDEXIT PROGRAM 14
B.1 Program Inputs 14
B.2 Program Outputs 14
B.3 Technical Requirements 14
B.4 Provided Batch File 15
B.5 Sample Program Call 15

C.0 BDBS RECORD LAYOUTS 16

D.0 ALS DATA EXTRACT 25

1.0 INTRODUCTION

The purpose of this manual is to describe the file organization and contents of the Broadcast Data Extract (AM-FM-TV). The data being provided is extracted from the Broadcast (AM-FM-TV) database system, commonly called BDBS. The Data Extract is sold to the Industry Canada (I.C.) clients on a yearly subscription basis by the Technical Information Service (DBC-E/TIS)

1.1 Changes

The BDBS extract is now provided in the same dBASEIII format that is used at Industry Canada.

The Consultant ASCII conversion program CONDUMP, is still provided but since it is no longer supported, it is now described in Appendix 1.

2.0 DISTRIBUTION AND MEDIA

The data extract is delivered as one complete copy of the data four times during the fiscal year.

The current media for distribution is DOS (Disk Operating System) formatted diskettes of 1.2 or
1.44 MB capacity. In the future, the data will be delivered on higher density media depending on demand (CD). Plans also call for the on-line BBS to be replaced by an Internet FTP site permitting easy access across Canada.

3.0 DATA AND FILE ORGANIZATION

The data comes from the Broadcast (AM-FM-TV) database system (BDBS) and is stored in dBASEIII format. The main index used to identify data is the station Call Sign. To uniquely identify stations, a two letter code (Banner) is added to the end of the Call Sign.

This Call Sign-Call Flag combination is used as the main index for Broadcast data.

3.1 Data Restrictions

Data on applications under consideration is confidential, and is not included in the data extract.
In the contours data table, negative values may appear in some Grade A, Grade B, 3000mV/m and 500mV/m contours. They indicate that those values are realistic contours. These negative contour points were calculated with a method different than the use of F(50,50) curves for TV and FM. Methods like Bullington or other propagation calculation programs were used.

In the future, a decision will be made to store only realistic contours, or to store separately F(50,50) and realistic contours under different names. AM service contours are currently not included in the data extract.

AM contours are being digitized for Digital Radio Broadcast (DRB) planning and will be made available as they are stored in the BDBS.
The BDBS and extract currently does not contain U.S. station contours. Negotiations are under way to see if they are available and can be included in the data extract.

As volume of data increases, it may become necessary to split the contours database table (CONTOURS.DBF) into three separate files for AM-FM-TV.

3.2 File Organization

The BDBS LAN system uses a standard dBASE storage format for the Broadcast data. The dBASE format of data storage was selected as being the most commonly used among PC users.

A file called BDBS_EXT.WP is provided with each full extract and provides descriptions of all the files produced.
     FILE	DESCRIPTION
 DBFPRINT.ZIP Display utility for dBase files
 DBSTP032.ZIP	Display/Write to a file the dBase structure
     AMSTATIO.DBF	Main station information for AM stations
 APATDAT.DBF	Data records for pattern points (FM, TV)
 APATDESC.DBF	Description record of patterns
 APATSTAT.DBF	Link of pattern keys to call sign/banners
 APATSTA2.NTX	Index of pattern keys
 AUGMENT.DBF	AM station augmentations
 CITY.DBF	Lookup table for station locations
 COMMENTS.DBF	Comments of all station types
 COMMENTS.DBT	Memo fields of COMMENTS.DBF
 CONTOURS.DBF	Station contours of FM and TV stations
 EXTEND.DBF	AM stations extended hours of operation
 FEEDS.DBF	Source of feed signals
 FMSTATIO.DBF	Main station information for FM stations
 PARAMS.DBF	AM stations parameters (towers information)
 PROVINCE.DBF	Lookup table for all stations
 REGION.DBF	Data that regional users supply
 REGION1.NTX	Index of regional files by CALLS_BANR
 TVSTATIO.DBF	Main station information for TV stations
 BDBS.DD	Data Dictionary
 CONDUMP.EXE	Program to create ASCII files
 CONS_DEF.DBF	Controlling database file to govern processing
 DB_2_ASC.BAT	Batch file for the CONDUMP conversion step
 PKUNZIP.EXE	Program to unzip compressed files
 BDBS_EXT.WP	This file
 E-LIMFMC.TXT	English text describing limitations to FM stations in Canada
 E-LIMFMU.TXT	English text describing limitations to FM stations in the United States
 F-LIMFMC.TXT	French text describing limitations to FM stations in Canada
 F-LIMFMU.TXT	French text describing limitations to FM stations in the United States
 E_LIMITS.TXT	English text describing limitations to TV stations in Canada
 F_LIMITS.TXT	French text describing limitations to TV stations in Canada
 INDEXIT.EXE	Index dBase file
     MAKENTX.BAT	Batch file to index files
4.0 ANTENNA PATTERNS

More and more TV and FM stations are using directional antennas. For this reason, a TV/FM directional antenna pattern database has been implemented. This database contains data on horizontal and vertical antenna patterns.

TV/FM Antenna pattern data is stored as relational information in four data files, APATSTAT.DBF, APATDESC.DBF, APATDAT.DBF and APATKEY.DBF. The diagram above shows the four data files along with the relationship existing between them.

Each TV/FM antenna pattern when added to the database is assigned a unique integer value referred to as the antenna pattern key (PATT_KEY). The pattern key permits to quickly identify and locate the antenna pattern information specific to a given station.
Record Layouts

APATKEY	The APATKEY file serves two purposes. First, it is used to maintain a listing of the theoretical antenna patterns currently saved in the database. Secondly, it is used to save the highest antenna pattern key currently assigned in the database (always stored in the very last record in the file). APATKEY is normally accessed to perform one of the following three operations:

   1-	To calculate a unique antenna pattern key to be assigned to a new theoretical or measured pattern being added to the database. The new key value is the key value retrieved from APATKEY last record incremented by one.
   2-	To obtain the antenna pattern key of a theoretical pattern. This is needed when adding a station having a theoretical pattern to the antenna pattern database.
   3-	To update the theoretical antenna patterns listing whenever adding or removing a theoretical pattern from the database.

Field #	Field Name	Type	Width	Description
1	S_NAME	C	12	'Special Name' field normally containing the name of the theoretical antenna patterns. The only exception is the file last record which contains the text 'LASTKUSED' indicating that the record holds the highest pattern key assigned.
2	PATT_KEY	N	6	Pattern key assigned to the theoretical pattern identified by the S_NAME field.

TABLE 1: APATKEY.DBF data fields.

The associated indexing file APATKEY1.NTX indexed on the S_NAME field permits to search for a theoretical pattern or for the 'LASTKUSED' record.

The associated indexing file APATSTA1.NTX indexed on the CALLS_BANR field permits to search for any given station call sign and banner combination.
APATKEY Data Sample:

S_NAME	PATT_KEY
OMNI	1
BAY-01	2
BAY-02	3
BAY-03	4
BAY-04	5
BAY-05	6
BAY-06	7
LASTKUSED	2542

APATSTAT	The APATSTAT.DBF file is basically a reference table providing 'station call sign' versus 'antenna pattern key' information. It permits to determine what antenna pattern key has been assigned to a given FM or TV station given the call sign and banner of the station.

Field #	Field Name	Type	Width	Description
1	CALLS_BANR	C	14	Station call sign (12 char.) concatenated with the station banner (2 char.).
2	PATT_KEY	N	6	Pattern key assigned to the station identified by the call sign and banner.

TABLE 2: APATSTAT.DBF data fields.

The associated indexing file APATSTA1.NTX indexed on the CALLS_BANR field permits to search for any given station call sign and banner combination.
Another indexing file, APATSTA2.NTX has an index build on the file's two fields: CALLS_BANR + STR(PATT_KEY)
APATSTAT Data Sample:

CALLS_BANR	PATT_KEY
CBCQ-TV-1 OP	1794
CBCQ-TV-1 OP	2405
CBCT OP	92
CBCT OP	176
CBCT-1 OP	93
CBCT-1 OP	1765
CBCT-1 OP	2371

APATDESC	The APATDESC file contains a single "header" type record describing the attributes of the antenna patterns. All the parameters describing the patterns are found in this file with the exception of the data points describing the actual patterns.
Field #	Field Name	Type	Width	Description
1	PATT_KEY	N	6	Pattern key.
2	HOR_VER	C	1	Orientation. "H" for horizontal and / Date pattern added to system "V" for vertical.
3	PATT_NUM	N	1	*Future use.
4	PATT_TYPE	C	12	Type of pattern: 'PRECISE', / 'BRIEF', / 'THEORETICAL'.
5	PUNITS	N	1	*Future use.
6	NUMPOINTS	N	3	Number of points in the pattern.
7	PATT_DATE	D	8	Date pattern added to system

TABLE 3: APATDESC.DBF data fields.
Note that PATT_NUMB and PUNITS are currently not used, and should not be counted on to contain valid data.
The associated indexing file APATDES1.NTX indexed on the PATT_KEY field permits to do a search based on the pattern key.
APATDESC Data Sample:

PATT_KEY	HOR_VER	PATT_NUMB	PATT_TYPE	PUNITS	NUMPOINTS	PATT_DATE
1	H	1	THEORETICAL	1	180	1/05/87
2	V	1	THEORETICAL	1	181	10/19/87
1794	H	0	PRECISE	1	65	01/07/94
2405	V	1	PRECISE	1	181	02/10/94
92	H	1	BRIEF	1	8	1/02/87
93	H	1	BRIEF	1	8	1/02/87
176	H	1	BRIEF	1	8	1/23/90
1765	H	0	PRECISE	1	45	01/31/94
2371	V	1	PRECISE	1	181	02/18/94

APATDAT	This file contains the 'gains' versus 'angle' data points defining the patterns. The record format permits to store one data point per record, therefore the storage of one pattern requires as many records as there are data points.

Field #	Field Name	Type	Width	Description
1	PATT_KEY	N	6	Pattern key.
2	ANGLE	N	8	Pattern data point azimuth from true north (degrees).
3	GAIN	N	12	Pattern data point gain at the given angle (dB).

TABLE 4: APATDAT.DBF data fields.

Two indexing files are associated with APATDAT.DBF. APATDA1.NTX is indexed on the PATT_KEY field and APATDA2.NTX is indexed on a key derived from two fields: STR(PATT_KEY,6) + STR(ANGLE,8,4)
APATDAT Data Sample:

PATT_KEY	ANGLE	GAIN
92	0.000	0.000
92	45.000	0.000
92	90.000	-1.9382
92	135.000	-9.354
92	180.000	-9.9601
92	25.00	-9.354
92	270.00	-1.9382
92	315.00	0.00
93	0.00	-9.837
93	45.00	-5.5128
93	90.0	-1.6858

Antenna Pattern Usage

As part of the analysis of broadcast undertakings, antenna pattern data is lifted from tables in the brief or digitized from diagrams of the horizontal and vertical pattern.

The PATT_TYPE field gives information on the source and/or relative prevision of the antenna pattern data.

When no vertical antenna pattern data appears in the brief, a theoretical pattern for an antenna with the same number of bays is selected. In this case PATT_TYPE is set to "THEORETICAL".

4.1 Omnidirectional Patterns

In the case of an Omnidirectional antenna, the Effective Radiated Power value from the main database is assumed to be the same for all azimuths. For this reason, no Horizontal pattern data is stored for Omnidirectional stations.

4.2 Vertical Patterns

As described in the record layouts, the HOR_VER field is used to indicate a (H)orizontal or (V)ertical pattern.
It is possible that a station with an Omnidirectional antenna may still have a Vertical antenna pattern, and this is supported.

4.3 "THEORETICAL " Patterns

Very often measured patterns are not available at the time of the brief's analysis. In such cases, the department uses theoretical vertical patterns based on the Cosine Law. They have names from BAY-2 to BAY-12, corresponding to the theoretical vertical patterns of a two bay antenna, up to that of a twelve bay antenna.

4.4 "BRIEF"/"PRECISE" Patterns

When pattern values area taken from a table in a technical brief, PATT_TYPE is set to "BRIEF". If the values are digitized from antenna diagrams, PATT_TYPE is set to "PRECISE".

5.0 FUTURE PLANS

BDBS is being converted to Oracle. The dBASE BDBS extract will continue to be produced under Oracle operations.

6.0 ALS DATA EXTRACT

This section refers to data obtained from the department's ALS (Automated Licensing System) database. This data is used in TV/LAND Mobile incompatibility studies and in non-ionizing radiation reports. The data is updated on a daily basis by the primary users. Complete extracts are obtained on a monthly basis. The data contains more than 240,000 records.

The Broadcast version resides in a 32MB dBASE file. At the present time, the ALS extract cannot list frequencies used by Police and other security agencies. Therefore, only records with divulgation code set to "1" will be released.

It is hoped that this data will be made available on CD media in the near future.
Appendix 1 part D. describes ALS Data Extract record layouts.

7.0 SUPPORT UTILITIES

Other AM/FM/TV engineering analysis programs area available through the DGRB/DGSE Technical Information Service (DBC-E/TIS). These programs have been revised to operate on the dBASE format data as provided in the Data Extract. For these programs to operate correctly, they require data indexes to exist for the dBASE formatted data files.

For reasons of efficient data distribution, these indexes are not provided on diskette when the Extract is sent out. Instead, an index creation program and batch file are supplied. Refer to the Appendix for information on the use of this Indexing utility.

Note that all support utilities included with the Data Extract are Shareware programs or programs written by Industry Canada staff or contractors. They have been tested at Industry Canada and to the best of our knowledge operate as described. They are provided for your convenience. Industry Canada, its employees, and contractors assume no responsibility for any loss or damage resulting from the use of these products, however caused.
8.0 CONTOURS ACCURACY

Note that the information stored in the CONTOURS.DBF file fields LAT_END and LONG_END are decimal degrees values representing the derived lattitude and longitude for that contour point. The point is described by the azimuth and distance stored in the same record, as calculated from the station site.

Differences in the values between the Contour file LONG_END (for azimuth of 0) and the longitude for the station site are to be expected since the station site longitude is stored as DDMMSS values. While the two longitudes appear to be different, they represent the same value in their respective units of storage.
APPENDIX 1

A.0 CONDUMP PROGRAM

The CONDUMP program was developed to 'dump' Broadcast information stored in dBASE format to ASCII file format, identical to the ASCII files distributed in the past. Since current policy is to discontinue the distribution of ASCII files, this program is offered to allow Consultant firms to perform their own conversion of dBASE files to ASCII format if desired.

The CONDUMP program creates ASCII files according to the specifications in document "Data Dump to Satisfy Outside Requests for Data, December 1986".

A.1 dBASE-to-ASCII Batch File

A batch file called DB_2_ASC.BAT is included with the dBASE files and CONDUMP program. Use this batch file, or refer to it to create your own file, when running the CONDUMP program.

Sample DB_2_ASC.BAT

 @ECHO OFF
 ::
 :: Batch file for the CONDUMP (Consultant Formatted dump) conversion step.
 :: Note the DOS variable set below : EXTRCT represents
 :: the disk directory where the input (DBF) files are located.
 :: This batch file assumes that you are located in the same directory as the CONDUMP.EXE and CONS_DEF.DBF files.
 ::
 SET CLIPPER=V010;F065;E1000
 SET EXTRCT=X:\TEMP
 ::
 CONDUMP
 ::
 :END
 SET CLIPPER=
 SET EXTRCT=
 :: A file called README.PLS (Read me, please) is provided with each full extract or update and provides descriptions of all the files produced.

A.2 Program Inputs

The CONDUMP program uses a controlling database file to govern processing. The file name is CONS_DEF.DBF, and it must be located in the same directory as the program file CONDUMP.EXE.

The program inputs are the data files (.DBF files) included on the distribution diskette. Note that the program searches for these files in the directory specified by DOS environment variable EXTRCT (eg. "D:\TEMP" or "L:\BCST\EXTRACT\DATA" ).
A.3 Program Outputs

Three ASCII files are produced ; AM_DUMP.ASC, FM_DUMP.ASC and TV_DUMP.ASC. They contain the dumped records for the three station types. These files are created in the current DOS directory where the CONDUMP program is executed.

The three major files, AM_DUMP.ASC, FM_DUMP.ASC and TV_DUMP.ASC provide information on stations in operation or authorized for operation.

The Record Layouts are listed in order of increasing number.

- Records 01 to 11 describe AM data,
- Records 21 to 31 describe FM data,
- Records 41 to 52 describe TV data.

The data is stored in ASCII code format and is separated in records of a length of 80 characters. Each record is numbered and corresponds to a group of data and to a type of station. The following table lists all the records available:

Record Content	Record Number

Station Data / Feeds Information / AM Antenna Parameters / Augmentation Data / Extended Hours of Operation Data / Applicant Name (comment no. 1) / Details on Limitations / EHAT Contour Data / 3 mV/m Service Contour Data (S3) / 500 uV/m Service Contour Data (S500) / A Service Contour Data / B Service Contour Data	AM / 01+02+03 / 04 / 05 / 06 / 10	FM / 21+22+23 / 26 / 28 / 30 / 31	TV / 41+42+4 / 3 / 44 / 47 / 47 / 49 / 51 / 52

Several records are created for each station. For every station, the first record indicates how many records are following (last field in records 01, 21 and 41).

Records 04, 05 and 06 for AM, 28 to 31 for FM, and 44 and 49 to 52 for TV can be repeated.

This is because these records list variables data that can have multiple occurrences (i.e. antenna parameters and augmentation).
A.4 Technical Requirements

To run the CONDUMP program, the following requirements should be met :

Free disk space should be at least equal to the size of the DBF database files to be converted.

Free conventional (low) RAM memory on your PC should be at least 480K.

DOS 3.3 or higher should be used.

The program should run in a DOS window if you prefer using Windows, assuming other requirements are met. Expect some performance slowdown if using this approach.

A.5 CONFIG.SYS

If using DOS 6.x and EMM386 (see CONFIG.SYS file), ensure the NOVCPI keyword is used in the EMM386 device statement in CONFIG.SYS.

ie.	DEVICE=C:\DOS\EMM386.EXE NOEMS NOVCPI .....

The CONFIG.SYS file should contain the following FILES and BUFFERS specifications as a minimum :

FILES=55
BUFFERS=20
B.0 INDEXIT PROGRAM

The INDEXIT program was developed to create index files for Broadcast data files stored in dBASE format. The program will operate on any xBase compatible database file.

B.1 Program Inputs

The program requires four parameters to control its operation as shown by the following syntax:

INDEXIT <DBFName ><Key Expression><Index name><[C|D]><[U]>

where
C|D = > Clipper (NTX) | dBASE (NDX) type indexing
U = Unique (No duplicate keys)
the fifth parameter <U> is optional and is not required.

Note that both <DBFName> and <Index name> may contain DOS path specifications. If no path information is provided, the current directory is assumed.

<Key Expression> must be a valid xBase expression. It may be a compound expression or a simple field name, but must meet xBase syntax requirements.

B.2 Program Outputs

INDEXIT creates the named index file<Index name>, based on the index expression <Key Expressions>. The file extension of the index file will be ".NTX" if a Clipper stye index was selected, or ".NDX" if a dBASE style was selected. The file is created in the current directory unless a path is specified as part of the file name.

A brief screen display appears to describe the indexing activity.

B.3 Technical Requirements

To run the INDEXIT program, the following requirements should be met:

Free disk space should be at least equal to the size of the anticipated index file. If in doubt, free disk space should equal or exceed the size of the database being indexed.

Free conventional (low) RAM memory on your PC should be at least 480K. DOS 3.3 or higher should be used.

The program should run in DOS windows if you prefer using Windows, assuming other requirements are met. Expect some performance slowdown if using this approach.
If INDEXIT is operating on a LAN, it assumes that it will have exclusive access to the database file being indexed. If it cannot gain this exclusive use of the file, no indexing is performed and the program returns an error code (DOS errorlevel) of 1.

Note that while the INDEXIT program does not overwrite any database information, any problems resulting from its usage are not the responsibility of Industry Canada or the author of the program.

B.4 Provided Batch File

A batch file named MAKENTX.BAT is provided with the INDEXIT program to show correct usage of the program. It may be used as a model for developing Indexing batch files for other applications. Part of the file is shown below as an illustration.

Not that if the desired index key is a compound expression (more than one field), the field names may be concatenated as shown in the italicized program call. Also note that NO imbedded blanks are permitted in the compound expression.

@ECHO OFF
::
::Creates required index files for IC supported
::programs. Assumes INDEXIT.EXE and databases are in current directory
::
INDEXIT apatstat CALL_BANR APATSTA1.NTX C
INDEXIT apatkey S_NAME APATKEY1.NTX C
INDEXIT FMSTATIO CALL_SIGN+BANNER FMSTATI1.NTX C
INDEXIT TVSTATIO CALL_SIGN+BANNER TVSTATI1.NTX C
::
:END

B.5 Sample Program Call

INDEXIT TVSTATIO CALL_SIGN+BANNER TVSTATI1.NTX C
        | | | |
        | | | Indicates Clipper style index
        | | Name of output Index file (.NTX optional)
        | Compound xBase expression (note "+" concatenation)
        Name of database index (.DBF assumed)

C.0 BDBS RECORD LAYOUTS

AMSTATIO.DBF "AM stations" Main station info for AM stations.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PROVINCE C 2 0 Province / State
 2 CITY C 20 0 City name
 3 CALL_SIGN C 12 0 Call sign of station
 4 FREQUENCY N 7 2 Frequency in kHz. Valid 530 to 1700.
 5 CLASS C 3 0 Class (A, B, C, CC, LP)
 6 LATITUDE N 7 0 N.Latitude of the AM
        Station's Transmitter.(ddmmss)
 7 LONGITUDE N 8 0 W.Longitude of the AM
        Station's Transmitter(dddmmss)
 8 BANNER C 2 0 Banner flag (A, C, O, P)
 9 STATUS1 C 2 0 Application Status day-time
10 STATUS2 C 2 0 Application Status night-time
11 LATITUDE2 N 7 0 Day-time N.latitude coordinate in degrees
        if site different than night-time site.
12 LONGITUDE2 N 8 0 Day-time W.longitude coordinate in degrees
        if site different than night-time site.
13 BRDR_LAT N 7 0 Latitude used when BORDER last calculated
14 BRDR_LONG N 8 0 Longitude used when BORDER last calculated
15 BORDER N 7 1 Closest distance to Canada US Border(km)
16 CAN_LAND N 7 1 Closest distance to Canada Land Edge
17 USA_LAND N 7 1 Closest distance to USA Land Edge
18 FRE_LAND N 7 1 Closest distance to French Land Edge near
        Newfoundland
19 ST_CREAT D 8 1 Date station entered in database
20 ST_MOD D 8 1 Date station last modified
21 OK_DUMP D 8 1 Last date of record update for the
        Consultants dump
22 DOC_FILE N 5 0 I.C.'s file number
23 DEC_NUMBER N 6 0 CRTC Decision Number
24 IFRBN_D N 5 0 IFRB Number for day time
25 IFRBN_N N 5 0 IFRB Number for night time
26 CLIST1 N 4 0 Change List number 1
27 CLIST2 N 4 0 Change List number 2
28 CLIST3 N 4 0 Change List number 3
29 CLIST4 N 4 0 Change List number 4
30 CLIST5 N 4 0 Change List number 5
31 CLIST6 N 4 0 Change List number 6
32 CLIST7 N 4 0 Change List number 7
33 CLIST8 N 4 0 Change List number 8
34 CLIST9 N 4 0 Change List number 9
35 CLIST10 N 4 0 Change List number 10
36 NETWORK C 4 0 Network (CBCE, CBCF, IND, INDE, INDF,
        BCMH, or none)
37 CERT_NUMB C 6 0 Broadcasting Certificate Number
        in format AANNNN
38 BC_MODE C 1 0 Broadcasting Mode (Stereo, Mono)
39 UNATTENDED C 1 0 Unattended Operation Code (Y, N)
40 AUTO_PROG C 1 0 Automatic Programming Code (Y, N)
41 EUVALU N 5 1 RSS Night Interference Free Value
42 POWERDAY N 7 0 Power in watts Day Time
43 PAR_RMS_D N 8 2 RMS value mV/m Day Time
44 Q_DAY N 7 2 Reduced Q factor Day Time
45 POWERNIGHT N 7 0 Power in watts Night Time
46 PAR_RMS_N N 8 2 RMS value mV/m Night Time
47 Q_NIGHT N 7 2 Reduced Q factor Night Time
48 POWERCRIT N 7 0 Power in watts Critical Hours of Operation
49 PAR_RMS_C N 8 2 RMS value during Critical hours of OPS.
50 Q_CRIT N 7 2 Reduced Q factor during Crit. hours OPS.
51 CHANNEL N 4 0 4 digit Frequency in kHz. Ex: 1250

APATDAT.DBF "Antenna PATtern DATa" Detail records for pattern points.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PATT_KEY N 6 0 Pattern key number used in all APAT files.
 2 ANGLE N 8 4 Angle in Degrees; AZIMUTH.
 3 GAIN N 8 4 RADIATION at ANGLE. (dB above ERPVPK)

APATDESC.DBF "Antenna PATtern DEScriptions" Description record of pattern.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PATT_KEY N 6 0 Pattern key number used in all APAT files.
 2 HOR_VER C 1 0 Pattern Type; H or V.
 3 PATT_NUMB N 1 0 Unused
 4 PATT_TYPE C 12 0 Type of Pattern; BRIEF, THEO, PRECISE
 5 PUNITS N 1 0 Unused
 6 NUMPOINTS N 3 0 Number of points in APATDAT file.
 7 PATT_DATE D 8 0 Last date of change

APATKEY.DBF "Antenna PATtern KEY" File holding pattern names and counter.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 S_NAME C 12 0 Station name "CALL_SIGN"
 2 PATT_KEY N 6 0 Pattern key number used in all APAT files.

APATSTAT.DBF "Antenna PATtern STAtion" Link of pattern keys to Callsign/banners.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station name "CALL_SIGN" + "BANNER"
 2 PATT_KEY N 6 0 Pattern key number used in all APAT files.

AUGMENT.DBF "AM station augmentations" "Many" child of AM stations
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 DNC_CODE C 1 0 D, N, C: Day, Night, Critical indicator
 3 NUMBER N 2 0 Augmentation segment number.
 4 RADIATION N 8 2 Radiation at central AZIMUTH (mV/m)
 5 CENTER_AZ N 5 1 Central AZIMUTH of Augmentation (degrees)
 6 SPAN N 5 1 Span of Augmentation (degrees)

CITY.DBF "City names" Lookup table for station locations
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PROVINCE C 2 0 Provincial or State code
 2 NAME C 20 0 City name.
 3 LATITUDE N 7 0 N.Latitude (city centre or 1st station)(ddmmss)
 4 LONGITUDE N 8 0 W.Longitude (city centre or 1st station)(dddmmss)
 5 CREAT_DT D 8 0 Date city record created
 6 MOD_DT D 8 0 Data city record modified

COMMENTS.DBF "Comments" "One" child of all station types.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 NAME C 40 0 Name of license
 3 ADDR1 C 40 0 Address line # 1
 4 ADDR2 C 40 0 Address line # 2
 5 ADDR3 C 40 0 Address line # 3
 6 ADDR4 C 40 0 Address line # 4
 7 HQCOMM M 10 0 General Headquarters comments
 8 RGCOMM M 10 0 General Regional comments
 9 EDETAILS M 10 0 Details on Limitations; English
10 FDETAILS M 10 0 Details on Limitations; French

CONTOURS.DBF "Station contours" "Many" child of FM and TV stations.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 AZIMUTH N 5 1 Azimuth; degrees from true North
 3 VALU_DIST N 10 4 Height in Meters above Sea Level
        or distance in kilometres between the
        transmitter site and the contour point.
 4 NAME C 4 0 Contour name; AM (EUN, 5000, 500D, 500N)
        FM (HAAT,3000, 500) TV (HAAT, GRDA, GRDB)
 5 LAT_END N 8 4 Calculated end-point N.latitude (decimal fraction)
 6 LONG_END N 8 4 Calculated end-point W.longitude(decimal fraction)

EXTEND.DBF "AM stations extended hours of operations" "Many" child of AM.
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 NUMBER N 2 0 Extended Period Number
 3 ANT_SYSTEM C 1 0 Antenna System Used for the Extended
        Operation (D, N)
 4 START1 C 4 0 Month and Day to Start the Extended
        Operation
 5 END1 C 4 0 Month and Day to End the Extended
        Operation
 6 START2 N 4 0 Hour and Minute to Start Extended
        Operation
 7 END2 N 4 0 Hour and Minute to End Extended
        Operation
 8 POWER N 7 0 Station's Power in Watts
 9 RMS N 7 2 RMS value of Radiation in mV/m at 1 Km

FEEDS.DBF "TV - source of feed signals" "Many" child of TV
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 FEED_ID C 1 0 Feed Identifier; A or B
 3 FEED_CHAN N 4 0 0, 2 - 83, or 2500 - 2680
 4 LINK_TYPE C 1 0 Type of FEED LINK; O, U, S, C
 5 FEED_CALL C 12 0 Name of the SOURCE of the FEED
 6 FEED_LAT N 7 0 N.Latitude of the FEED SOURCE(ddmmss)
 7 FEED_LONG N 8 0 W.Longitude of the FEED SOURCE(dddmmss)
FMSTATIO.DBF "FM stations"
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PROVINCE C 2 0 Province / State code
 2 CITY C 20 0 City name.
 3 CALL_SIGN C 12 0 Call sign of station
 4 FREQUENCY N 7 2 Frequency in MHz 88.1 to 107.9
 5 CLASS C 3 0 Class of Station; A, A1, B, B1, C, C1, C2,
        D, LP, VLP; For Canadian Stations, A, A1, B,
        C, C1, LP, VLP; For Non-Canadian Stations,
        A, B, B1, C, C1, C2, D
 6 LATITUDE N 7 0 N.Latitude of the FM
        Station's Transmitter(ddmmss)
 7 LONGITUDE N 8 0 W.Longitude of the FM
        Station's Transmitter(dddmmss)
 8 BANNER C 2 0 AL, AP, AU, CP(US Only), DE, IC, IL, OP, PC,
        RE, TD, TO, UA, UC, UN: Allotment, Approved,
        Authorized, Construction Permit, Denied,
        Incomplete, Illegal, Operational, Proposed
        Channel, Referred to CRTC, Tentative
        Deletion, Temp. Operation, Approved by CRTC,
        Under Consideration, Unacceptable
 9 SS_CODE C 5 0 Short Spacing Code; "*O#aa"
10 NETWORK C 4 0 Network affiliation: CANC, CBC, CBCE, CBCF,
        IND, INDE, INDF, Space
11 ANT_MODE C 1 0 Antenna Mode; O, D; Omnidirectional or
        Directional
12 BC_MODE C 1 0 Broadcasting Mode: S, M, Space; Stereo,
        Mono
13 BRDR_LAT N 7 0 N.Latitude used when BORDER last calculated
14 BRDR_LONG N 8 0 W.Longitude used when BORDER last calculated
15 BORDER N 7 1 Closest distance to Canada US Border(km)
16 CAN_LAND N 7 1 Closest distance to Canada Land Edge
17 USA_LAND N 7 1 Closest distance to USA Land Edge
18 FRE_LAND N 7 1 Closest distance to French Land Edge near
        Newfoundland
19 ST_CREAT D 8 1 Date station entered in the database
20 ST_MOD D 8 1 Date station was last modified
21 OK_DUMP D 8 1 Last date of record Modification for a
        Consultants dump
22 DOC_FILE N 5 0 I.C. file number; any 5 Numeric digits
23 DEC_NUMBER N 6 0 CRTC Decision Number "YYNNNN"
24 UNATTENDED C 1 0 Unattended Operation Code (Y, N)
25 CERT_NUMB C 6 0 Broadcasting Certificate Number "FANNNN"
26 SCMO C 1 0 Subsidiary Carrier Multiple Operation Code
        Y or N
27 AUTO_PROG C 1 0 Automatic Programming Code; Y, N
28 BEAM_TILT N 5 1 Beam Tilt Angle in Degrees; -10.0 to 10.0
29 EHAATT N 7 1 Effective Height of Antenna Above Terrain
        -1,200.0 to 2,000.0 meters
30 ERPVAV N 7 0 ERP Vertical Average in Watts
31 ERPVPK N 7 0 ERP Vertical Peak Power in Watts
        0 to over 5,000,000
32 ERPHAV N 7 0 ERP Horizontal Average in Watts
        0 to over 360,000
33 ERPHPK N 7 0 ERP Horizontal Peak Power in Watts
        0 to over 360,000
34 GROUND_LEV N 6 1 Ground Level at Tower Base above Sea Level
        in Meters: 0.0 to 9,999.9
35 OVERALL_H N 5 1 Overall Height Above ground in Meters
        0.0 to 999.9 meters
36 RAD_CENTER N 6 1 Radiating Center Above Mean Sea Level
        0.0 to 5000.0 metres
37 CHANNEL N 4 0 Channel 201 to 300

PARAMS.DBF "AM stations parameters - (towers information)"
 # FIELD NAME TYPE LEN DEC "Many" child of AM
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 DNC_CODE C 1 0 Parameter Group Code; D, N, C;
        Day, Night, Critical.
 3 TOWER_NUMB N 2 0 Tower number
 4 FIELDRATIO N 7 4 Field Ratio
 5 SPACING N 9 4 Spacing in Degrees
 6 ORIENTA N 8 4 Orientation in Degrees
 7 PHASING N 9 4 Phasing in Degrees
 8 HEIGHT N 5 1 Height in Degrees
 9 TYPE_ANT N 2 0 Type of Antenna Structure
10 A N 8 4 Tower Field A; Valid 0 to 360.0000.
11 B N 8 4 Tower Field B; Valid 0 to 360.0000.
12 C N 8 4 Tower Field C; Valid 0 to 360.0000.
13 D N 8 4 Tower Field D; Valid 0 to 360.0000.

PROVINCE.DBF "Description of provinces" Lookup table for all stations
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PROVINCE C 2 0 Province Code
 2 COUNTRY C 2 0 Country Code
 3 LOW_LAT N 7 0 Province bounding box, lower latitude
 4 HIGH_LAT N 7 0 Province bounding box, high latitude
 5 LOW_LONG N 8 0 Province bounding box, lower longitude
 6 HIGH_LONG N 8 0 Province bounding box, high longitude
 7 CREAT_DT D 8 0 Creation date of Province Record
 8 MOD_DT D 8 0 Modification Date
 9 ENGDESC C 25 0 Name of province/state; English
10 FRNDESC C 25 0 Name of province/state; French

REGION.DBF "Data from regional offices" Data that regional users supply
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 CALLS_BANR C 14 0 Station identification
 2 REGION C 1 0 Regional Code; P,C,Q,A,O
 3 DISTRICT C 2 0 District Code; 11-18, 22-26, 31-34, 41-46,
        48, 49, 51-55, 59, 61, 63, 65, 66, 69
 4 INSPEC_REP C 1 0 Inspection Report Code; Space, S, U
 5 PAINTING C 4 0 Painting or Lighting Code; F, B, L, S, P,
        Space; Flashing, Beacon, Lighting,
        Strobe, Painting.
 6 SPR_DAT D 8 0 Supplementary Proof:
 7 RSP_DAT D 8 0 Request for Proof:
 8 STDETT D 8 0 Consultant Test Start:
 9 AIR_CLEAR D 8 0 "On Air" clearance date
10 INSPEC_DAT D 8 0 Last inspection date
11 RCF_DAT D 8 0 Consultant Retained:
12 STAT_TYPE C 2 0 Type of station (AM, FM, TV)
13 DOCFEX C 4 0 Inspection Report Code:
14 PROVINCE C 2 0 Province code
15 COUNTRY C 2 0 Country code

TVSTATIO.DBF "TV stations"
 # FIELD NAME TYPE LEN DEC
--------------------------------
 1 PROVINCE C 2 0 Province / State
 2 CITY C 20 0 City name
 3 CALL_SIGN C 12 0 Station call sign
 4 FREQUENCY N 7 2 Frequency in MHz. (too many to list)
 5 CLASS C 3 0 Class of Station; A, B, C, D, F, N, R, S, LP,
        VLP
 6 LATITUDE N 7 0 Latitude coordinate in degrees of the
        Station's Transmitter
 7 LONGITUDE N 8 0 Longitude coordinate in degrees of the
        Station's Transmitter
 8 BANNER C 2 0 AL, AP, AU, CP, DE, IC, IL, OP, PC, RE, TD,
        TO, UA, UC, UN; Allotment, Approved,
        Authorized, Construction Permit, Denied,
        Incomplete, Illegal, Operational, Proposed
        Channel, Referred to CRTC, Tentative
        Deletion, Temp. Operation, Approved by CRTC,
        Under Consideration, Unacceptable
 9 LIMITE C 5 0 Limitation Identification code "LAAAA"
10 NETWORK C 4 0 Network; AECC, ASN, CANC, CBCE, CBCF, CTV,
        GTN, HC, INDE, INDF, KNOW, MITV, MM, NN,
        PATV, R-QF, TSN, TVA, TVO, and Space
11 ANT_MODE C 1 0 Antenna Mode: O, D, Space; Omnidirectional
        or Directional
12 BC_MODE C 1 0 Broadcasting Mode; S, P, B, Space; Stereo,
        Second Audio Channels or Both
13 OFFSET C 1 0 Refers to TV Off-set Code. Space, +, -, Z.
14 OFF_PREC C 1 0 Refers to Off-set Precision. Valid Y, Space.
15 BRDR_LAT N 7 0 Latitude used when BORDER last calculated
16 BRDR_LONG N 8 0 Longitude used when BORDER last calculated
17 BORDER N 7 1 Closest distance to Canada US Border(km)
18 CAN_LAND N 7 1 Closest distance to Canada Land Edge
19 USA_LAND N 7 1 Closest distance to USA Land Edge
20 FRE_LAND N 7 1 Closest distance to French Land Edge near
        Newfoundland
21 ST_CREAT D 8 1 Date station entered in database
22 ST_MOD D 8 1 Date station last modified
21 OK_DUMP D 8 1 Last date of record Modification for a
        Consultants dump
24 DOC_FILE N 5 0 I.C. file number
25 DEC_NUMBER N 6 0 CRTC Decision Number: "YYNNNN"
26 UNATTENDED C 1 0 Unattended Operation Code (Y, N)
27 CERT_NUMB C 6 0 Broadcasting Certificate Number "TANNNN"
28 CLOSE_CAP C 1 0 Closed Captioning; Y or N
29 ALLOC_ZONE N 1 0 Allocation Planning Zone 0, 1 or 2
30 BEAM_TILT N 5 1 Beam Tilt Angle in Degrees; -10.0 to 10.0
31 EHAATT N 7 1 Effective Height of Antenna Above Terrain
        -1,200.0 to 2,000.0 meters
32 ERPVAV N 7 0 ERP Visual Average in Watts
33 ERPVPK N 7 0 ERP Visual Peak Power in Watts
        0 to over 5,000,000
34 ERPAAV N 7 0 ERP Aural Average in Watts
        0 to 1,000,000
35 ERPAPK N 7 0 ERP Aural Peak Power in Watts
        0 to 1,000,000
36 ERPVTA N 7 0 ERP Peak Visual Power at Tilt Angle in Watts
        0 to more than 5,000,000
37 ERPATA N 7 0 ERP Average Power at Tilt Angle in watts
        0 to 5,000,000
38 GROUND_LEV N 6 1 Ground Level at Tower Base above Sea Level
        in Meters: 0.0 to 9,999.9
39 OVERALL_H N 5 1 Overall Height Above ground in Meters
        0.0 to 999.9
40 RAD_CENTER N 6 1 Radiating Center Above Ground Level
        0.0 to 5,000.0 metres
41 CHANNEL N 4 0 CHANNEL; 2 - 83, or 2,500 - 2,680

NOTES:
- Latitudes are currently expressed in degrees, positive for Northern
 Hemisphere and negative for Southern Hemisphere.
 Unless otherwise indicated latitudes are expressed in +-DDMMSS.

- Longitudes are currently expressed in positive degrees only and have
 the meaning of West. Some longitudes exceed 180 degrees.
 Unless otherwise noted longitudes are expressed in +-DDDMMSS.

- Unless otherwise noted, antenna heights are in meters(m) and distance
 is expressed in kilometres(km)

        Listing index keys 11 Jan 94 10:51:08
        ===========================================

The following index key expressions are utilized for data processing within the Broadcast Database system at Industry Canada. They are provided as a guide when using the included Index Creation Utility.

Index file Key expression
--------------------------------------------------------
AMSTATI1.NTX CALL_SIGN+BANNER
AMSTATI2.NTX CITY
AMSTATI3.NTX SUBSTR(STR(LONGITUDE,7,0),1,3) + SUBSTR(STR(LATITUDE,6,0),1,2)
AMSTATI4.NTX CHANNEL
APATDAT1.NTX PATT_KEY
APATDAT2.NTX STR(PATT_KEY,6)+STR(ANGLE,8,4)
APATDES1.NTX PATT_KEY
APATKEY1.NTX S_NAME
APATKEY2.NTX PATT_KEY
APATSTA1.NTX CALLS_BANR
APATSTA2.NTX CALLS_BANR+STR(PATT_KEY)
AUGMENT1.NTX CALLS_BANR
AUGMENT2.NTX CALLS_BANR+DNC_CODE
AUGMENT3.NTX CALLS_BANR+DNC_CODE+STR(NUMBER)
BDBSDIC1.NTX ALIAS
BDBSREP1.NTX RI_REPORT
BDBS_ER1.NTX ERRCODE
BDBS_SY1.NTX DATAPATH
CITY1.NTX PROVINCE+NAMEData dictionary of ALS data extract for Broadcast use

Structure for database: P:\ALS\DIV1\ALSDIV1.DBF
Number of records : 219212
Last update : 93/07/08
-----------------------------------------------
Field Field Name Type Length Dec Description
   1 LICENSEE Character 25 Licensee name
   2 COMPNY_COD Numeric 10 Company code
   3 DISTRICT Numeric 2 IC District office No
   4 DIV_CODE Numeric 1 Divulgation code
        (1)freely distributable
        (2)do not divulgate
*** F.G. WARNING *** Do NOT rely exclusively on this field
*** You MUST NOT disclose also
   Company codes starting with 17...........
        0217.........
        0817.........
        0917.........
        1017.........
        1217.........
        1517.........
        5217.........
        5617.........
*******************************************************************

   5 CALL_SIGN Character 10 Station Callsign
   6 LOCATION Character 25 Region,city,province
        unformatted
   7 LATITUDE Numeric 6 North latitude of tx
   8 LONGITUDE Numeric 7 West longitude of tx
**** F.G. of Station could be a RX only *****
   9 SITE_ELEV Numeric 5 Ground level in feet(meters)?
**** F.G. site elevation -MTRS AMSL ***********
  10 FREQ_TX Numeric 13 6 Tx frequency in MHz
  11 FREQ_RX Numeric 13 6 Rx frequency in MHz

  12 STATUS Numeric 1 Status of Station
**** F.G. Frequency status
    Status - 0 - Pending
        1 - Individually authorized
        2 - Authorized to be billed
        3 - Authorized for future
        4 - Invoiced
        5 - Authorized paid/licence held
        6 - Active
        7 - Under reconsideration
        8 - Transferred
        9 - Cancelled ******
  13 ERP_DBW Numeric 5 1 tx Effective Radiated Power
  14 ELEV_ANGLE Numeric 7 3 Elevation angle from horizon
        of main beam in degrees
*** F.G. TX antenna elevation angle - beam tilt from horizontal ground *****
  15 ANT_HEIGHT Numeric 4 height of antenna Radiation
        centre above mean sea level
        in meters?
*** F.G. TX antenna height AGL-MTRS of radiating elements ******
  16 AZIMUTH Numeric 5 1 Azimuth of main beam (degrees
        from True North).
*** F.G. Azimuth from true north of antenna's direction of maximum radiation ***
  17 ANT_GAIN Numeric 4 1 antenna gain in dbW
  18 AZM_MLOBE Numeric 5 1 Azimuth of main lobe (degrees
        from True North).
*** F.G. TX antenna beamwidth - Half power beamwidth distance of 3dB from the antenna **

  19 ANTMOD_NO Character 8 Antenna mode
*** F.G. Antenna model number ****
-----------------------------------------------
** Total ** 157

CITY2.NTX PROVINCE
COMMENT1.NTX CALLS_BANR
CONTOUR1.NTX CALLS_BANR
CONTOUR2.NTX CALLS_BANR+NAME
CONTOUR3.NTX CALLS_BANR+NAME+STR(AZIMUTH,5,1)
DATES1.NTX CALLS_BANR
EXTEND1.NTX CALLS_BANR
EXTEND2.NTX CALLS_BANR+ANT_SYSTEM+STR(NUMBER,2)
FEEDS1.NTX CALLS_BANR
FEEDS2.NTX CALLS_BANR+FEED_ID
FMSTATI1.NTX CALL_SIGN+BANNER
FMSTATI2.NTX CITY
FMSTATI3.NTX SUBSTR(STR(LONGITUDE,7,0),1,3) + SUBSTR(STR(LATITUDE,6,0),1,2)
KEYWORDS.NTX longwd
LOGIN1.NTX LOGID
LOOKUP1.NTX FIELDNAME
LOOKUP2.NTX FIELDNAME+CODE
PARAMS1.NTX CALLS_BANR
PARAMS2.NTX CALLS_BANR+DNC_CODE+STR(TOWER_NUMB)
PROVINC1.NTX PROVINCE
REGION1.NTX CALLS_BANR
SCREEN1.NTX TABLE
TVSTATI1.NTX CALL_SIGN+BANNER
TVSTATI2.NTX CITY
TVSTATI3.NTX SUBSTR(STR(LONGITUDE,7,0),1,3) + SUBSTR(STR(LATITUDE,6,0),1,2)

D.0 ALS DATA EXTRACT

Data dictionary of ALS data extract for Broadcast use

Structure for database: P:\ALS\DIV1\ALSDIV1.DBF
Number of records : 219212
Last update : 93/07/08
-----------------------------------------------
Field Field Name Type Length Dec Description
   1 LICENSEE Character 25 Licensee name
   2 COMPNY_COD Numeric 10 Company code
   3 DISTRICT Numeric 2 IC District office No
   4 DIV_CODE Numeric 1 Divulgation code
        (1)freely distributable
        (2)do not divulgate
   5 CALL_SIGN Character 10 Station Callsign
   6 LOCATION Character 25 Region,city,province
        unformatted
   7 LATITUDE Numeric 6 North latitude of tx, rx
   8 LONGITUDE Numeric 7 West longitude of tx, rx
   9 SITE_ELEV Numeric 5 Ground level in meters above
mean sea level
  10 FREQ_TX Numeric 13 6 Tx frequency in MHz
  11 FREQ_RX Numeric 13 6 Rx frequency in MHz
  12 STATUS Numeric 1 Status of Station
        0 - Pending
        1 - Individually authorized
 2 - Authorized to be billed
        3 - Authorized for future
        4 - Invoiced
        5 - Authorized paid/licence held
        6 - Active
        7 - Under reconsideration
        8 - Transferred
        9 - Cancelled ******
  13 ERP_DBW Numeric 5 1 tx Effective Radiated Power
  14 ELEV_ANGLE Numeric 7 3 Elevation angle from horizon
in degrees
  15 ANT_HEIGHT Numeric 4 Height of antenna Radiation
        centre above ground in meters
  16 AZIMUTH Numeric 5 1 Azimuth of main beam (degrees
        from True North).
  17 ANT_GAIN Numeric 4 1 Antenna gain in dbW
  18 AZM_MLOBE Numeric 5 1 Degrees of half power beamwidth (3dB)	in degrees of the antenna
  19 ANTMOD_NO Character 8 Antenna model number
-----------------------------------------------
** Total ** 157